## Slide 1: The checked hilltop result was correct
VIPER site maps, Oct 27 2027

## Slide 2: The reported result
The map shows a hilltop in shadow.
The side of the same hill is lit.
This result required a terrain check.

## Slide 3: The Sun was below the local horizontal plane
The Sun was 3 degrees below the local horizontal plane. The shaded band shows the relevant part of the cycle.

## Slide 4: Terrain can block the Sun at the hilltop
Sunlight reaches the site from below the local horizontal plane.
Terrain receives direct light where the Sun is above its terrain horizon.
A slope can receive light while nearby terrain blocks light at the hilltop.

## Slide 5: Cross section of the measured hill
Light reaches the steep flank. A limiting ray passes approximately 1 meter above the hilltop.

## Slide 6: Observer height changes the result
At 1 meter observer height, the hilltop pixel receives part of the solar disk. At ground level, it remains in shadow.
For a fixed blocker 13 meters away, a 1 meter height change gives an angular change of approximately 4 degrees.
The map values agree with the independent terrain calculation.
Chart: 
| 0 m | 0.25 m | 0.5 m | 1 m
Hilltop (% lit) | 0 | 0 | 0 | 50
Hillside (% lit) | 0 | 0 | 84 | 100

## Slide 7: Investigation result
The checks found no renderer defect in this case.
The checks used the renderer, independent terrain geometry, and Sun-position calculations.
Use tools/debug/probe_pixel.jl to examine a site pixel.